23-11-2010

ECE 233 Midterm

Q-1- For the circuit below show that the voltage at point D (node D) is equal to.

Q-2-

a) Find the first order differential equation for the state variable Vc(t) for the circuit below.

b) The differential equation governing a state variable x(t) is given by . It is also known that the initial condition for the state variable is x(0)=2. Find x(t) when .

Hint: The particular solution is

Q-3-

a) The waveform y(t) is given in the figure below. Write y(t) as the combination of unit step “u(t)” and unit ramp “r(t)” functions.

b) For the capacitor (C=1 Farad) in Figure 1, the current applied to the capacitor is shown Figure 2.

The applied current is . The initial condition for the capacitor voltage is  Volt. Find Vc(t) when 0≤t.

Figure 1                               Figure 2

Q-4- For the circuit below the initial condition for the capacitor voltage is Vc(0-)=5 Volt.

The switch SW is initially open and it is closed when t=0. Find the values for Vc(0+), Ic(0-), and Ic(0+).