11-01-2013

ECE 233 Final

Q-1- A series RLC circuit is shown in the figure below. The state variables of this circuit are IL(t) and VC(t).

a) Find the state space representation where the state vector is (10 point)

b) Find the second order differential equations for the state variables IL(t) and VC(t). (10 point)

Q-2- The first order differential equations of a second order circuit is given below.

This circuit is fed by an impulsive voltage source VS(t)=δ(t) Volt. The initial conditions of the state variables are given as VC(0-)=1 Volt and IL(0-)= 1 Amper. Find the initial conditions after the application of the impulsive source (What are VC(0+) and IL(0+), , ). (10 point)

Q-3- A Series first order RL circuit is given below.

The resistance value R=1Ω and the inductance L=1 Henry.

- Find the differential equation governing the state variable IL(t). (5 point)

- If the applied input VS(t)=sin(t) t≥0 what is the particular solution of the differential equation governing IL(t). (5 point)

Q-4- The input applied to the circuit below is given by the mathematical formula

The switches S1 and S2 are initially open (when second) and they are then closed  when . The circuit parameters are given as L=1 Henry, C1=1 Farad, C2=3 Farad, R=0.25 Ω. The initial conditions are given as Vc(0)=0 Volt, IL(0)=0 Amper, Vc2(0)= Volt. Find Vc(t) and IL(t) when . (40 point)

Q-5- Find the Voltage-Current (V-I) characteristics of the circuit below. The diodes in the circuit are ideal Va=2 Volt, Vb=2 Volt. R1=2200 Ω, R2=1000 Ω, R3=1000 Ω. (20 point)