ECE 232

# Lab1

# First order circuits

## Preliminary Work:

1. Consider the circuit and the input voltage waveform Vin(t) (which is a square wave with some DC value) on Figure. Take V1=1V and V2=3V.

Figure 1: The circuit                                  Figure 2: The input waveform Vin(t)

a. Obtain the differential equation for the circuit. For the values of f, R and C in Table 1, determine and sketch VC(t) and VR(t). Calculate the time constant for each case.

|  | f (kHz) | R (k) | C (nF) |
| --- | --- | --- | --- |
| 1 | 2 | 3.3 | 4.7 |
| 2 | 2 | 3.3 | 10 |
| 3 | 2 | 68 | 10 |

### Table1

b. Replace the capacitor in Figure with an indictor L. Obtain the differantial equation and for the values of f, R, and L in Table 1, determine and sketch  VL(t) and VR(t) for the input in part 1. Calculate in each case.

| f (kHz) | R (k) | L (H) |
| --- | --- | --- |
| 2 | 3.3 | 0.1 |
| 2 | 1.8 | 0.1 |
| 10 | 3.3 | 0.1 |

Table2

c. How can be found experimentally from the voltage waveforms seen on oscilloscope screen?  Hint: Consider the exponential characteristics of voltage waveforms in one interval.

Experimental Work

1. Adjust the square wave output of the function generator as in Preliminary Work part 1.

a. Set up the circuit on the Figure 1. For the values of f, R and C in the Table 1, observe and plot the AC components of Vin(t), VC(t) and VR(t), also note the DC levels in each case. Determine the time constant of the circuits experimentally.

b. Replace the capacitor C with the inductor L and repeat part 1.a for the values of f, R and C in the Table 2.

Equipment List: Resistors: 1.8kΩ, 3.3kΩ, 68kΩ, Capacitors: 4.7nF, 10nF, Inductors: 100mH